## Slide 1: Advanced Computer Architecture Lecture 1 – Introduction, A simple RISC processor
Yasir Javed
Abasyn University Islamabad Campus
Most of course slides from CS152 and CS252 UC Berkeley

## Slide 2: What is Computer Architecture?
Application
Physics
Gap too large to bridge in one step
In its broadest definition, computer architecture is the design of the abstraction layers that allow us to implement information processing applications efficiently using available manufacturing technologies.
(but there are exceptions, e.g. magnetic compass)

## Slide 3: Abstraction Layers in Modern Systems
Algorithm
Gates/Register-Transfer Level (RTL)
Application
Instruction Set Architecture (ISA)
Operating System/Virtual Machines
Microarchitecture
Devices
Programming Language
Circuits
Physics
Comp. Arch

## Slide 4: Architecture continually changing
Compatibility
Cost of software development makes compatibility a major force in market
Applications
Technology
Applications suggest how to improve technology, provide revenue to fund development
Improved technologies make new applications possible

## Slide 5: Computing Devices Then…
EDSAC, University of Cambridge, UK, 1949

## Slide 6: Computing Devices Now
Robots
Supercomputers
Automobiles
Laptops
Set-top boxes
Smart phones
Servers
Media Players
Sensor Nets
Routers
Cameras
Games

## Slide 7: Moore’s Law
“Cramming More Components onto Integrated Circuits”
  Gordon Moore, Electronics, 1965
# on transistors on cost-effective integrated circuit double every 18 months

## Slide 8: Uniprocessor Performance
VAX : 25%/year 1978 to 1986
RISC + x86: 52%/year 1986 to 2002
RISC + x86: ??%/year 2002 to present
From Hennessy and Patterson, Computer Architecture: A Quantitative Approach, 4th edition, October, 2006
What happened????

## Slide 9: Limiting Force: Power Density

## Slide 10
[from Kurzweil]
Major Technology Generations
Bipolar
nMOS
CMOS
pMOS
Relays
Vacuum Tubes
Electromechanical
?

## Slide 11: Single-Thread Processor Performance
[ Hennessy & Patterson, 2017 ]

## Slide 12: Upheaval in Computer Design
Most of last 50 years, Moore’s Law ruled
  Technology scaling allowed continual performance/energy improvements without changing software model
Last decade, technology scaling slowed/stopped
  Dennard (voltage) scaling over (supply voltage ~fixed)
  Moore’s Law (cost/transistor) over?
  No competitive replacement for CMOS anytime soon
  Energy efficiency constrains everything
No “free lunch” for software developers, must consider:
  Parallel systems
  Heterogeneous systems

## Slide 13: Today’s Dominant Target Systems
Mobile (smartphone/tablet)
  >1 billion sold/year
  Market dominated by ARM-ISA-compatible general-purpose processor in system-on-a-chip (SoC)
  Plus sea of custom accelerators (radio, image, video, graphics, audio, motion, location, security, etc.)
Warehouse-Scale Computers (WSCs)
  100,000’s cores per warehouse
  Market dominated by x86-compatible server chips
  Dedicated apps, plus cloud hosting of virtual machines
  Now seeing increasing use of GPUs, FPGAs, custom hardware to accelerate workloads
Embedded computing
  Wired/wireless network infrastructure, printers
  Consumer TV/Music/Games/Automotive/Camera/MP3
  Internet of Things!

## Slide 14: A Simple RISC Processor Basic Building Blocks

## Slide 15: Hardware Elements
Combinational circuits
  Mux, Demux, ALU, ...
Synchronous state elements
  Flipflop, Register, Register file, SRAM, DRAM
Edge-triggered: Data is sampled at the rising edge
Clk
D
Q
En
ff
Q
D
Clk
En
OpSelect
- Add, Sub, ...
- And, Or, Xor, Not, ...
- GT, LT, EQ, Zero, ...
Result
Comp?
A
B
ALU
Sel
O
A0
A1
An-1
Mux
.
.
.
lg(n)
Sel
O
De
Mux
.
.
.
lg(n)

## Slide 16: Register Files
ReadData1
ReadSel1
ReadSel2
WriteSel
Register
file
2R+1W
ReadData2
WriteData
WE
Clock
rd1
rs1
rs2
ws
wd
rd2
we
Reads are combinational
ff
Q0
D0
Clk
En
ff
Q1
D1
ff
Q2
D2
ff
Qn-1
Dn-1
...
...
...
register

## Slide 17: Register File Implementation
reg 31
rd
clk
reg 1
wdata
we
rs1
rdata1
rdata2
reg 0
…
32
…
5
32
32
…
rs2
5
5
  RISC-V integer instructions have at most 2 register source operands
Register files with a large number of ports are difficult to design
  Intel’s Itanium, GPR File has 128 registers with 8 read ports and 4 write ports to support 4 integer operations per cycle!!!

## Slide 18: A Simple Memory Model
MAGIC
RAM
ReadData
WriteData
Address
WriteEnable
Clock
Reads and writes are always completed in one cycle
  a Read can be done any time (i.e. combinational)
  a Write is performed at the rising clock edge
  if it is enabled
   the write address and data
  must be stable at the clock edge
Later in the course we will present a more realistic model of memory

## Slide 19: Administrivia
Instructor: Yasir Javed, yasir.javed@abasyn.edu.pk
Text: Computer Architecture: A Quantitative Approach,
Hennessey and Patterson
Other Reference Material:
Computer organization and Design,The hardware/software interface, Patterson and Hennessey.
UC berkeley CS152 and CS252 course material
Videos are uploaded on Renzym Education channel. Go to playlist section and open computer architecture playlist
Youtube Link: www.youtube.com/renzymeducation
Notes: This slide is for the 3-min class administrative matters.
Make sure we update Handout #1 so it is consistent with this slide.

## Slide 20: CS152 Structure and Syllabus
Six modules
  Simple machine design (ISAs, microprogramming, unpipelined machines, Iron Law, simple pipelines)
  Memory hierarchy (DRAM, caches, optimizations) plus virtual memory systems, exceptions, interrupts
  Complex pipelining (score-boarding, out-of-order issue)
  Explicitly parallel processors (vector machines, VLIW machines, multithreaded machines)
  Multiprocessor architectures (memory models, cache coherence, synchronization)
  (If time allows) Multi-threading, Latency Tolerance, GPU, Power, Warehouse Scale Computing
Notes: This is the 1st slide of the “Course Structure and Course Philosophy” section of the lecture.
Need to emphasis that for exams, our goal is the test your knowledge. It is not our goal to test how well your perform under time pressure.

## Slide 21: Instruction Set Architecture (ISA)

## Slide 22: RISC-V ISA
New RISC design from UC Berkeley
Realistic & complete ISA, but open & small
Not over-architected for a certain implementation style
Both 32-bit and 64-bit address space variants
  RV32 and RV64
Designed for multiprocessing
Efficient instruction encoding
Easy to subset/extend for education/research
We’ll be using 32-bit RISC-V this semester in lectures, very similar to MIPS

## Slide 23: RV32 Processor State
Program counter (pc)
32x32-bit integer registers (x0-x31)
x0 always contains a 0
32 floating-point (FP) registers (f0-f31)
each can contain a single- or double-precision FP value (32-bit or 64-bit IEEE FP)
FP status register (fsr), used for FP rounding mode & exception reporting

## Slide 24: RISC-V Instruction Formats
Destination Reg.
Reg. Source 1
Reg. Source 2
7-bit opcode field (but low 2 bits =112)
Additional opcode bits/immediate

## Slide 25: R-Type/I-Type/R4-Type Formats
Reg. Source 3
12-bit signed immediate
Reg-Reg ALU operations
Reg-Imm ALU operations
Load instructions, (rs1 + immediate) addressing
Only used for floating-point fused multiply-add

## Slide 26: B-Type
12-bit signed immediate split across two fields
Branches, compare two registers, PC+immediate target
(Branches do not have delay slot)
Store instructions, (rs1 + immediate) addressing, rs2 data

## Slide 27: L-Type
Writes 20-bit immediate to top of destination register.
Used to build large immediates.
12-bit immediates are signed, so have to account for sign when building 32-bit immediates in 2-instruction sequence (LUI high-20b, ADDI low-12b)

## Slide 28: J-Type
“J” Unconditional jump, PC+offset target
“JAL” Jump and link, also writes PC+4 to x1
Offset scaled by 1-bit left shift – can jump to 16-bit instruction boundary (Same for branches)

## Slide 29: Implementing RISC-V: Single-cycle per instruction datapath & control logic

## Slide 30: Instruction Execution
Execution of an instruction involves
    1. instruction fetch
    2. decode and register fetch
    3. ALU operation
    4. memory operation (optional)
    5. write back
and the computation of the address of the
next instruction

## Slide 31: Datapath: Reg-Reg ALU Instructions
RegWrite Timing?
5 5 5 10 7
rd rs1 rs2 func opcode rd  (rs1) func (rs2)
31 27 26 22 21 17 16 7 6 0
0x4
Add
clk
addr
inst
Inst.
Memory
PC
Inst<26:22>
Inst<21:17>
Inst<31:27>
Inst<16:0>
OpCode
ALU
ALU
Control
RegWriteEn
clk
rd1
GPRs
rs1
rs2
wa
wd
rd2
we

## Slide 32: Datapath: Reg-Imm ALU Instructions
5 5 12 3 7
rd rs1 immediate12 func opcode rd  (rs1) op immediate
31 27 26 22 21 10 9 7 6 0
Imm
Select
ImmSel
inst<21:10>
OpCode
0x4
Add
clk
addr
inst
Inst.
Memory
PC
ALU
RegWriteEn
clk
rd1
GPRs
rs1
rs2
wa
wd
rd2
we
inst<26:22>
inst<31:27>
inst<9:0>
ALU
Control

## Slide 33: Conflicts in Merging Datapath
Imm
Select
ImmSel
OpCode
0x4
Add
clk
addr
inst
Inst.
Memory
PC
ALU
RegWrite
clk
rd1
GPRs
rs1
rs2
wa
wd
rd2
we
inst<26:22>
Inst<31:27>
Inst<21:10>
Inst<16:0>
ALU
Control
Inst<9:0>
Introduce
muxes
rd rs1 immediate12 func3 opcode rd  (rs1) op immediate
5 5 5 10 7
rd rs1 rs2 func10 opcode rd  (rs1) func (rs2)
Inst<21:17>

## Slide 34: Datapath for ALU Instructions
<16:0>
rd rs1 immediate12 func3 opcode rd  (rs1) op immediate
5 5 5 10 7
rd rs1 rs2 func10 opcode rd  (rs1) func (rs2)
Op2Sel
Reg / Imm
Imm
Select
ImmSel
OpCode
0x4
Add
clk
addr
inst
Inst.
Memory
PC
ALU
RegWriteEn
clk
rd1
GPRs
rs1
rs2
wa
wd
rd2
we
<26:22>
<21:17>
FuncSel
ALU
Control
<31:27>
<6:0>

## Slide 35: Load/Store Instructions
WBSel
ALU / Mem
rs1 is the base register
rd is the destination of a Load, rs2 is the data source for a Store
Op2Sel
“base”
disp
ImmSel
OpCode
FuncSel
ALU
Control
ALU
0x4
Add
clk
addr
inst
Inst.
Memory
PC
RegWriteEn
clk
rd1
GPRs
rs1
rs2
wa
wd
rd2
we
Imm
Select
clk
MemWrite
addr
wdata
rdata
Data
Memory
we
rd rs1 immediate12 func3 opcode Load
5 5 5 7 3 7 Addressing Mode
imm rs1 rs2 imm func3 opcode Store (rs) + displacement

## Slide 36: RISC-V Conditional Branches
Compare two integer registers for equality (BEQ/BNE) or signed magnitude (BLT/BGE) or unsigned magnitude (BLTU/BGEU)
12-bit immediate encodes branch target address as a signed offset from PC, in units of 16-bits (i.e., shift left by 1 then add to PC).
7
6
0
opcode
3
9
7
func3
7
16
10
imm[6:0]
5
21
17
rs2
5
26
22
rs1
5
31
27
imm[11:7]
BEQ/BNE
BLT/BGE
BLTU/BGEU

## Slide 37: Conditional Branches (BEQ/BNE/BLT/BGE/BLTU/BGEU)
0x4
Add
PCSel
clk
WBSel
MemWrite
addr
wdata
rdata
Data
Memory
we
Op2Sel
ImmSel
OpCode
Bcomp?
FuncSel
clk
clk
addr
inst
Inst.
Memory
PC
rd1
GPRs
rs1
rs2
wa
wd
rd2
we
Imm
Select
ALU
ALU
Control
Add
br
pc+4
RegWrEn
Br Logic

## Slide 38: RISC-V Unconditional Jumps
25-bit immediate encodes jump target address as a signed offset from PC, in units of 16-bits (i.e., shift left by 1 then add to PC). (+/- 16MB)
JAL is a subroutine call that also saves return address (PC+4) in register x1
J
JAL
7
6
0
opcode
25
31
7
Jump Offset[24:0]

## Slide 39: RISC-V Register Indirect Jumps
Jumps to target address given by adding 12-bit offset (not shifted by 1 bit) to register rs1
The return address (PC+4) is written to rd (can be x0 if value not needed)
The RDNPC instruction simply writes return address to register rd without jumping (used for dynamic linking)
7
6
0
opcode
3
9
7
func3
12
21
10
Imm[11:0]
5
26
22
rs1
JALR
RDNPC
5
31
27
rd

## Slide 40: Full RISCV1Stage Datapath (Lab1)

## Slide 41: Hardwired Control is pure Combinational Logic
combinational
logic
op code
Equal?
ImmSel
Op2Sel
FuncSel
MemWrite
WBSel
WASel
RegWriteEn
PCSel

## Slide 42: ALU Control & Immediate Extension
Inst<6:0> (Opcode)
Decode Map
Inst<16:7> (Func)
ALUop
0?
+
FuncSel
( Func, Op, +, 0? )
ImmSel
( IType12, BsType12,
BrType12)

## Slide 43: Hardwired Control Table
Opcode | ImmSel | Op2Sel | FuncSel | MemWr | RFWen | WBSel | WASel | PCSel
ALU |  |  |  |  |  |  |  | 
ALUi |  |  |  |  |  |  |  | 
LW |  |  |  |  |  |  |  | 
SW |  |  |  |  |  |  |  | 
BEQtrue |  |  |  |  |  |  |  | 
BEQfalse |  |  |  |  |  |  |  | 
J |  |  |  |  |  |  |  | 
JAL |  |  |  |  |  |  |  | 
JALR |  |  |  |  |  |  |  | 
Op2Sel= Reg / Imm WBSel = ALU / Mem / PC
WASel = rd / X1 PCSel = pc+4 / br / rind / jabs
*
*
*
no
yes
rind
PC
rd
jabs
*
*
*
no
yes
PC
X1
jabs
*
*
*
no
no
*
*
pc+4
BrType12
*
*
no
no
*
*
br
BrType12
*
*
no
no
*
*
pc+4
BsType12
Imm
+
yes
no
*
*
pc+4
*
Reg
Func
no
yes
ALU
rd
IType12
Imm
Op
pc+4
no
yes
ALU
rd
pc+4
IType12
Imm
+
no
yes
Mem
rd

## Slide 44: Single-Cycle Hardwired Control: Harvard architecture
We will assume
  clock period is sufficiently long for all of
  the following steps to be “completed”:
      1. instruction fetch
      2. decode and register fetch
      3. ALU operation
      4. data fetch if required
      5. register write-back setup time
         tC > tIFetch + tRFetch + tALU+ tDMem+ tRWB
  At the rising edge of the following clock, the PC,
  the register file and the memory are updated

## Slide 45: Increasing Processor Clock Speed Pipeling RISC-V

## Slide 46: An Ideal Pipeline
All objects go through the same stages
No sharing of resources between any two stages
Propagation delay through all pipeline stages is equal
The scheduling of an object entering the pipeline
is not affected by the objects in other stages
stage
1
stage
2
stage
3
stage
4
These conditions generally hold for industrial assembly lines, but instructions depend on each other!

## Slide 47: Pipelined RISC-V
To pipeline RISC-V:
First build RISC-V without pipelining with CPI=1
Next, add pipeline registers to reduce cycle time while maintaining CPI=1

## Slide 48: Unpipelined Datapath for RISC-V
0x4
RegWriteEn
Add
Add
clk
WBSel
MemWrite
addr
wdata
rdata
Data
Memory
we
WASel
Op2Sel
ImmSel
OpCode
FuncSel
clk
clk
addr
inst
Inst.
Memory
PC
rd1
GPRs
rs1
rs2
wa
wd
rd2
we
Imm
Select
ALU
ALU
Control
1
PCSel
br
rind
jabs
pc+4
Bcomp?
Br Logic

## Slide 49: Hardwired Control Table
Opcode | ImmSel | Op2Sel | FuncSel | MemWr | RFWen | WBSel | WASel | PCSel
ALU |  |  |  |  |  |  |  | 
ALUi |  |  |  |  |  |  |  | 
LW |  |  |  |  |  |  |  | 
SW |  |  |  |  |  |  |  | 
BEQtrue |  |  |  |  |  |  |  | 
BEQfalse |  |  |  |  |  |  |  | 
J |  |  |  |  |  |  |  | 
JAL |  |  |  |  |  |  |  | 
JALR |  |  |  |  |  |  |  | 
Op2Sel= Reg / Imm WBSel = ALU / Mem / PC
WASel = rd / X1 PCSel = pc+4 / br / rind / jabs
*
*
*
no
yes
rind
PC
rd
jabs
*
*
*
no
yes
PC
X1
jabs
*
*
*
no
no
*
*
pc+4
BrType12
*
*
no
no
*
*
br
BrType12
*
*
no
no
*
*
pc+4
BsType12
Imm
+
yes
no
*
*
pc+4
*
Reg
Func
no
yes
ALU
rd
IType12
Imm
Op
pc+4
no
yes
ALU
rd
pc+4
IType12
Imm
+
no
yes
Mem
rd

## Slide 50: Pipelined Datapath
Clock period can be reduced by dividing the execution of an instruction into multiple cycles
tC > max {tIM, tRF, tALU, tDM, tRW} ( = tDM probably)
However, CPI will increase unless instructions are pipelined
write
-back
phase
fetch
phase
execute
phase
decode & Reg-fetch
phase
memory
phase
addr
wdata
rdata
Data
Memory
we
ALU
Imm
Select
0x4
Add
addr
rdata
Inst.
Memory
rd1
GPRs
rs1
rs2
wa
wd
rd2
we
IR
PC

## Slide 51: “Iron Law” of Processor Performance
Time = Instructions Cycles Time
Program Program * Instruction * Cycle
Instructions per program depends on source code, compiler technology, and ISA
Cycles per instructions (CPI) depends upon the ISA and the microarchitecture
Time per cycle depends upon the microarchitecture and the base technology
Microarchitecture | CPI | cycle time
Microcoded | >1 | short
Single-cycle unpipelined | 1 | long
Pipelined | 1 | short

## Slide 52: CPI Examples
Time
Inst 3
7 cycles
Inst 1
Inst 2
5 cycles
10 cycles
Microcoded machine
3 instructions, 22 cycles, CPI=7.33
Unpipelined machine
3 instructions, 3 cycles, CPI=1
Inst 1
Inst 2
Inst 3
Pipelined machine
3 instructions, 3 cycles, CPI=1
Inst 1
Inst 2
Inst 3
5-stage pipeline CPI≠5!!!

## Slide 53: Technology Assumptions
Thus, the following timing assumption is reasonable
A small amount of very fast memory (caches)
backed up by a large, slower memory
Fast ALU (at least for integers)
Multiported Register files (slower!)
tIM tRF tALU tDM  tRW
A 5-stage pipeline will be the focus of our detailed design
- some commercial designs have over 30 pipeline stages to do an integer add!

## Slide 54: 5-Stage Pipelined Execution
time t0 t1 t2 t3 t4 t5 t6 t7 . . . .
instruction1 IF1 ID1 EX1 MA1 WB1
instruction2 IF2 ID2 EX2 MA2 WB2
instruction3 IF3 ID3 EX3 MA3 WB3
instruction4 IF4 ID4 EX4 MA4 WB4
instruction5 IF5 ID5 EX5 MA5 WB5
Write
-Back (WB)
I-Fetch (IF)
Execute (EX)
Decode, Reg. Fetch (ID)
Memory (MA)
addr
wdata
rdata
Data
Memory
we
ALU
Imm
Select
0x4
Add
addr
rdata
Inst.
Memory
rd1
GPRs
rs1
rs2
wa
wd
rd2
we
IR
PC

## Slide 55: 5-Stage Pipelined Execution Resource Usage Diagram
time t0 t1 t2 t3 t4 t5 t6 t7 . . . .
IF I1 I2 I3 I4 I5
ID I1 I2 I3 I4 I5
EX I1 I2 I3 I4 I5
MA I1 I2 I3 I4 I5
WB I1 I2 I3 I4 I5
Resources
Write
-Back (WB)
I-Fetch (IF)
Execute (EX)
Decode, Reg. Fetch (ID)
Memory (MA)
addr
wdata
rdata
Data
Memory
we
ALU
0x4
Add
addr
rdata
Inst.
Memory
rd1
GPRs
rs1
rs2
ws
wd
rd2
we
IR
PC
Imm
Select

## Slide 56: Pipelined Execution: ALU Instructions
IR
IR
IR
1
PC
A
B
Y
R
MD1
MD2
addr
inst
Inst
Memory
0x4
Add
IR
Imm
Select
ALU
rd1
GPRs
rs1
rs2
wa
wd
rd2
we
wdata
addr
wdata
rdata
Data
Memory
we
Not quite correct!
We need an Instruction Reg (IR) for each stage

## Slide 57: Acknowledgements
These slides contain material developed and copyright by:
  Arvind (MIT)
  Krste Asanovic (MIT/UCB)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)
MIT material derived from course 6.823
UCB material derived from course CS252